## Slide 1
Instructor Name : Eng. El Hosein Ahmed
Advanced
Security
Profiles
FortiGate
Prepared by :
1- Ebrahim Sabry Farouk
2-Hussein Hisham Hussein
3- Ahmed Samy Abdallah Shokr
4-Mohamed Rabia fathi
5-Ahmed maged mohamed
6-Bishoy remon fahmy

## Slide 2
Project Overview
This project focuses on designing and implementing a fully secured enterprise network infrastructure.
The goal is to build a scalable multi-VLAN network with redundancy, security, dynamic routing, and integration with FortiGate firewalls.

## Slide 3
Network Architecture Model
The network follows a hierarchical enterprise model:
Core Layer
Distribution Layer (DSW-1 & DSW-2)
Access Layer (Finance, Marketing, Sales, HR, IT)

## Slide 4
VLAN
The network contains five main VLANs:
  VLAN 10 – Finance – 192.168.1.0/24
Structure
  VLAN 20 – Marketing – 192.168.2.0/24
  VLAN 30 – Sales – 192.168.3.0/24
  VLAN 40 – HR – 192.168.4.0/24
  VLAN 50 – IT – 192.168.5.0/24

## Slide 5
SVI
SVIs configured on distribution switches:
DSW-1:
  VLAN 10 → 192.168.1.254
  VLAN 20 → 192.168.2.254
  VLAN 30 → 192.168.3.254
  VLAN 40 → 192.168.4.254
  VLAN 50 → 192.168.5.254
DSW-2: Uses .253 as backup gateway for all VLANs.
Configuration

## Slide 6
VTP Configuration
  VTP Domain: cisco.com
  Password: 123
  DSW-1: Server Mode
  DSW-2: Server Mode
  Access Switches: Client Mode

## Slide 7
Trunking & DTP
  All uplinks configured as 802.1Q trunks
  Allowed VLANs: 10, 20, 30, 40, 50
  Native VLAN: 100
  DSWs: Dynamic Desirable
  Access Switches: Dynamic Auto

## Slide 8
Port Security
Applied on access-layer user ports:
  Max 2 MAC addresses
  Sticky MAC enabled
  Violation mode: Restrict
  PortFast enabled for end-user ports

## Slide 9
Redundancy
HSRP:
  Virtual Gateway: 192.168.x.100
  DSW-1 active for VLANs 10,20,30
  DSW-2 active for VLANs 40,50
(HSRP + STP)
STP:
  Priorities tuned to match HSRP roles for optimal traffic flow

## Slide 10
EtherChannel
Layer-3 EtherChannel between DSW-1 & DSW-2:
  Port-Channel 10
  DSW-1: 11.1.1.1/30
  DSW-2: 11.1.1.2/30
  Mode: ON

## Slide 11
  OSPF Area: 0
  Runs on Core & Distribution switches
  SVIs are passive
  Advertises:
    All VLAN networks
    Inter-switch links
OSPF Dynamic Routing

## Slide 12
FortiGate

## Slide 13
FortiGate Interface
Three main interfaces:
  LAN Interface: connected to core switch
  WAN Interface: provides Internet access
  Management Interface: secure admin access only
Configuration

## Slide 14
OSPF Dynamic VLAN
  OSPF enabled on the FortiGate
  Firewall learns all VLANs dynamically from Core switch
  Reduces manual configuration
  Improves scalability
Learning

## Slide 15
Firewall
1. LAN → WAN Policy:
  Allows internal users to access Internet
  NAT enabled
2. WAN → LAN Policy:
  Allows external access to published internal services
  Secured by filtering profiles
Policies

## Slide 16
Security Profiles Applied
Antivirus:
  Applied on inbound WAN → LAN traffic
  Protects against malware/viruses
Web Filter:
  Applied on LAN → WAN
  Blocks harmful & non-business websites
Application Control:
  Blocks social media and productivity-reducing apps

## Slide 17
IPsec VPN
A site-to-site VPN tunnel was configured:
  Phase 1 & Phase 2 completed
  Tunnel up and stable
  Routing configured between sites
  Specific VPN policy created
Connectivity

## Slide 18
Routing on FortiGate
  Default Route: 0.0.0.0/0 → WAN gateway
  Inter-branch routing via:
    Static routes or
    OSPF through the VPN tunnel

## Slide 19
High Availability (HA)
  Active–Passive HA configuration
  Automatic failover
  Ensures high uptime and business continuity

## Slide 20
Full Network Integration
The FortiGate firewall integrates fully with the Cisco-based network:
  Learns VLANs dynamically via OSPF
  Secures all inbound & outbound traffic
  Provides VPN connectivity
  Works with enterprise VLAN segmentation
  Enhances reliability via HA

## Slide 21
Conclusion
This combined Cisco + FortiGate design delivers:
  High security
  Full redundancy
  Scalable multi-VLAN architecture
  Branch connectivity
  Enterprise-grade protection
The network is ready for expansion and advanced security enhancements.

## Slide 22
Thank you for your attention!